## Slide 1
Snom 802.1x
Automatic provisioning
Notes: 1

## Slide 2
Basic Steps
Prepare CA
Create certificates
create snom provisioning files
create 802.1x snom .tar file
Notes: 2
Our Solution got a wide range of functionality and an intuitive use. We do work with System Intergrators but re and manage projects for medium sizes companies also ourself. The average size of our installation has approximately 400 users. We offer turn-key solutions for fixed and mobile business communication needs.

## Slide 3
Prerequisites
Radius Server / Linux (*Radius) or Windows (NPS), CISCO etc.
Local Provisioning https cert web server (opt. User data web server)
Guest provisioning VLAN with MAB Mac Access Bypass and phone client authentication
Secure 802.1x ideally with IEEE 802.1x VLAN Assignment VLAN

## Slide 4
Step by Step
Local Provisioning web server
From factory reset, redirect to local provisioning server
  DNS
  DHCP Option
  Internet access and snom redirect service
Client authentication enabled
  Snom Root CA http://wiki.snom.com/Category:HowTo:TLS

## Slide 5
Step by Step (Guest or Staging)
Guest provisioning VLAN with MAB Mac Access Bypass and phone client authentication
Connect Factory resetted phone
Switch support MAB and opens network to provisioning web server
Web server check snom phone client certificate against snom CA
Phone pulls Initial 802.1x snom provisioning file

## Slide 6
Step by Step (Guest or Staging)
Secure 802.1x ideally with IEEE 802.1x VLAN Assignment VLAN
Phone pulls User data snom provisioning file from
  Cert web server
  User Data web server
Phone is ready to call

## Slide 7
http://www.cisco.com/c/en/us/td/docs/solutions/Enterprise/Security/TrustSec_1-99/IP_Tele/IP_Telephony_DIG.html

## Slide 8
http://www.cisco.com/c/en/us/td/docs/solutions/Enterprise/Security/TrustSec_1-99/IP_Tele/IP_Telephony_DIG.html

## Slide 9
What more?
Certificate expires
  Secure provisioning already done, certificates can be changes
Snom phone PASS-Through needed?